## Slide 1: Design of a Novel Flash Translation Layer with Efficient Utilization of Spare Area

## Slide 2: Outline
Introduction
Related works
Motivation
Design
Experiments
Conclusion

## Slide 3: Introduction
Flash memory
  Small size
  Shock resistance
  Power-saving
  Light weight
Notes: In place update : 一筆 data 在某個 page 當中被寫入了，如果這筆 data 被 update 了，不能在同一個 physical page 中再寫一次，而必須在另一個 free page 寫入更新的資料。這就是 out-of-place update.
如果這個已經被寫過的 page 如果還要再被寫入新資料，就那要先 erase 過一次，才能再寫入新資料，就這就叫做 erase before write 的特性

## Slide 4: Introduction
2015/1/30
4
Flash Memory
physical block
( 32-128 pg )
Physical page
......
......
Main area
Spare area
........
2 - 4 KB
64 – 128 B
Read / write access unit
erase unit
Notes: 4

## Slide 5: Introduction
2015/1/30
5
physical block A
........
Data C
  Drawback : The erase-before-write property
  Out of place update
physical block B
........
Data C
Notes: 5

## Slide 6: Introduction
Flash Translation Layer
  Address translation
    Translate the logical page to the physical page in NAND flash memory
  Garbage collection
    Reclaim one free block for the current write request
      Switch merge, partial merge, full merge

## Slide 7: Introduction
Garbage collection
  Switch merge ; Partial merge
1
2
3
4
1
2
3
4
5
6
3
4
Switch merge
partial merge

## Slide 8: Introduction
Garbage collection
  Full merge
5
6
7
8
1
2
3
4
3
4
7
8
Full merge

## Slide 9: Related Work
Superblock scheme
    Record page-mapping information in spare area and block-mapping information in main memory
Mem
PPN
LPN
LBN
Page offset
Spare area
page
Spare area
page

## Slide 10: Related Work
Superblock scheme
  Block-level spatial locality
    One superblock is composed of N adjacent logical blocks
    Page map N adjacent logical blocks into N + M physical blocks. ( N = 4 , 0<= M <= 4 )
      N : data block; M : update block.
  Rearranging pages in several blocks
    Pages of one superblock could located at anywhere of N+M physical blocks
    Hybrid mapping with 3-level mapping table
      Fetch mapping info. from spare area two times and memory
      Limited size of spare area ( 64 bytes )
Notes: 說明 M 個 physical block 的意義。為什麼 N 個 logical block 不能放在 N 個 physical block ?
理論上， 4 個 logical block 有 256 個 pages, 應該需要 256 PBN 才能完全定址到這 256 個 logical pages 才對。但是 Superblock scheme 把這 256 個 logical page 放在固定 ( N+M ) 個 PBNs 裡, 所以 256 個 logical page 全都會在這 ( n+m ) 個 physical block 裡面

## Slide 11: Related Work
Superblock scheme
2015/1/30
11
17
Logical block
( 64 pages )
Subgroup
( 16 pages )
Logical page
( 1 pages )
0 – 15
16 - 31
32 - 47
48 - 63
0
63
31
…..
16
31
17
16
Logical block
( 64 pages )
Notes: 11

## Slide 12: Related Work
Superblock FTL
2015/1/30
12
Logical block
( 64 pg )
0 – 15
16 - 31
32 - 47
48 - 63
0
63
Subgroup
( 16 pg )
PTE_SIZE : 16
31
…..
16
31
17
16
PTE page 1
PTE page 2
PTE page 3
PTE page 0
PMD page
PGD table
LBN
……..
PMD index
( LPN / PTE_SIZE)
PTE index
( LPN % PTE_SIZE)
Q : How to find logical page 17 ?
Notes: 12

## Slide 13: Related Work

## Slide 14: Spare area In Superblock scheme
PBMT( 7PBNs)
Physical block
PPN
Block index
Page index
    All pages belonging to one superblock use the same PBMT

## Slide 15: Motivation
The limitation of Superblock scheme
  Only 8 physical blocks could be allocated to one superblock
    Restrict the superblock size.
    Limited share degree of the update block.
  Superblock scheme has to trigger self garbage collection if 8 physical blocks are full
    Trigger garbage collection more early

## Slide 16: Design goal
Extended-SuperBlock ( ESB ) FTL
  Upholding the advantages and eliminating the limitations of the Superblock scheme
    Covert the mapping structure for better flexibility
      No upper bound of physical blocks for each superblock
      Reconfigure superblock size

## Slide 17: Design
Covert the mapping structure
  Each subgroup has its own PBMT
  Lower the subgroup size to 8 logical pages for containing 8 PBNs in spare area
  ESB FTL plans two kind of spare area format
    PTE page, PMD page
0 – 15
16 - 31
32 - 47
48 - 63
0
63
4 x 16
0 – 7
56 - 63
0
63
8 – 15
16– 23
24– 31
…
8 x 8

## Slide 18: Spare area of PTE pages
  Its PBMT primarily records PBNs related to the specified subgroup
0 – 7
56 - 63
0
63
8 – 15
16– 23
24– 31
…
8 x 8
PTE page

## Slide 19: Spare area of PMD pages
Its PBMT primarily records PBNs related to PMD pages of the same logical block.
0 – 7
56 - 63
0
63
8 – 15
16– 23
24– 31
…
8 x 8
PMD page

## Slide 20: Mapping structure
ESB FTL scheme
2015/1/30
20
Subgroup
( 8 pg )
PTE_SIZE : 8
31
…..
24
31
25
24
PTE page 3
PMD page
PGD table
LBN
……..
0 – 7
56 - 63
0
63
8 – 15
16– 23
24– 31
…
8 x 8
PTE page 7
PTE page 0
PTE page 1
PTE page 2
…
PMD page 7 
PMD page 0 
PMD page 1 
PMD page 2 
……
ESB FTL : 64 PBNs / LBN
7 PBNs
Notes: 20

## Slide 21: Mapping structure
How to decide the type of a written page ?
PMD page
  The ending logical page of its related subgroup
  The last written page in the write request
PTE page
  Other than PMD pages, they are PTE pages
    The most useful PTE pages comes before the PMD pages because it holds the most whole information about its subgroup
21
Notes: 21

## Slide 22: Mapping structure
It’s good to write PMD page and PTE page at the same write request.
  But there are exceptions that occur when single page write request coming.
22
1
2
3
..
..
..
0
1
2
3
4
5
phy_blk 255
4
5
..
..
..
0
1
2
3
4
5
phy_blk 127
6
..
..
..
0
1
2
3
4
5
phy_blk 63
..
7
..
..
..
0
1
2
3
4
5
phy_blk 31
..
PMD pages sometimes have to point to its related logical page directly and use one PBN.
Notes: 22

## Slide 23: Mapping structure
Why write dummy ?
  When the PBNs in PMD pages are all occupied, and upper case happened, ESB FTL has to copy the valid PTE page to the free page, and then write the PMD page

## Slide 24: Write dummy example
Try to write logical page 7
24
1
2
3
..
..
..
0
1
2
3
4
5
phy_blk 255
4
5
..
..
..
0
1
2
3
4
5
6
..
..
..
0
1
2
3
4
5
phy_blk 63
..
0
1
2
3
4
5
4
7
phy_blk 127
phy_blk 31

## Slide 25: Evaluation
We develop a trace-driven simulator in order to evaluate the performance of ESB FTL
Parameters | Values
Number of Blocks | 655360 ( 80GB )
Update blocks | 16384 blocks ( 2.5% )
Pages Per Block | 64
Erase Block Time | 2000us
Page Write Time | 263 us
Page Read Time | 88 us

## Slide 26: Evaluation
Traces characteristic :
Traces | Descriptor
Linux PC | Ten-days of user activities under Ext3 file system
Win PC | One weeks of user activities under NTFS
Postmark | Workload of the mail server
Large File | Workload of copying a 4.5 GB DVD ISO file

## Slide 27: Experiment
GC overhead V.S. different Trace
  ESB is composed of 32 logical block

## Slide 28: Experiment
Space utilization of victim blocks
  ESB is composed of 32 logical block
  Win PC trace

## Slide 29: Experiment
GC overhead V.S. superblock size
  PostMark trace

## Slide 30: Experiment
GC overhead V.S. superblock size
  WinPC trace

## Slide 31: Conclusion
We have developed an ESB FTL upholding the advantages and eliminating the limitations of the Superblock scheme.
  We have lower the garbage collection overhead compared to Superblock scheme.
  ESB FTL achieves page-level mapping for each logical page by utilizing the spare area.
31
Notes: 31