## Slide 1
TINR
2019 Q1 VHV support

## Slide 2
LPPS MK4 introduction support – System Hardware Setup Tool
CLM ACPD issues – Task 630

## Slide 3: Improvement from LPPS MK3 to MK4
The main performance driver for LPPS MK4 is the increase in Spectral Radiance with a factor 1.7x (weighted average) when compared to the LPPS MK2/3.
  LPPS MK4: 1.6x
  Coating CL2Shutter fiber: 1.06x
  --------------------------------------
  Total radiance increase 1375: 1.7x
Improved diagnostics and communication to the laser.
Minimize Cost of Goods and make volume available
   Removal of Color filtering functionality/ shutterbox w/o attenuator
Radiance improvement in LPPS 1.27x  1.6x:
Redesign laser focus optics
New QCM coating  Al2O3
Reuse IR light

## Slide 4: Support LPPS MK4 introduction - System Hardware Setup Tool
The hardware setup tool prepares the system for recovery after a spare part swap or hardware upgrade.
It achieves this by setting the correct configuration and equipment constants

## Slide 5: SHST support
Reset configuration constants and ECs depending on the selected scenarios.
5 newly introduced error/warning codes for SHST to support LPPS MK4 introduction.

## Slide 6: Performance task 630 – CLM Spectral performance
602
603
Calibration tasks
Create spectra to encoder position table
Correct offset of spectra to encoder position for selected wavelengths
630
602
603
Drift
Measured spectra
Report
Performance tasks
Time required: 44 min
Time required: 5 min
Notes: If both |Δ𝜆|≤0.05 nm (WavelengthOffsetOkLimitCW) and |"Δ" 𝛬|≤0.3 nm, then no correction is necessary
Else if either |Δ𝜆|≥5 nm or |Δ𝛬|≥5 nm, finish the calibration as usual for all CW SET and BW SET
Else if either |Δ𝜆|> WavelengthOffsetWarningLimitCW or |Δ𝛬|> WavelengthOffsetWarningLimitBW
l_SET_NEW = 2*l_SET-l_GET; BW_SET_NEW = 2 * BW_SET-BW_GET

## Slide 7: Performance task 630 - Issues
Issue 1- Task #630 wants to apply the #603 correction without running it
Fix 1 - Input setting “Execute corrected step” to False only for YS375 machines. The other machines should have the same old default values for this input setting
Issue 2 - 1375 CL module task #630 fails when running it a second time with different input settings, only way to run is to add drift measurement
Fix 2 - Always removing duplicates from the WL-BW combinations lists before running the task.
Issue 3 - CLM task #630 reporting fails when only one bandwidth is selected - figure building requests at least 2 bandwidths
Fix 3 –
  Code is handling the number of unique BWs in a generic way (1 -> ∞)
  In case of 2WL-1BW combinations, the dimensions for the X-axis and Y-axis are calculated in a better way

## Slide 8: Lesson learned
Participate in LPPS MK4 introduction
Understand SHST operation mechanism -> useful for swapping of other components or upgrading.
Calibration task 603 is not supported for YS 375 and is only supported for YS 1375.

## Slide 10: SHST – newly introduced error/warning codes
Error - The missing of copyLPPSfirmware.bat
Error – Hardware and Firmware not match
Error – Firmware upgrading while lamp is on
Error – Firmware upgrade failure due to network not working
Warning - Firmware update skipped because latest version already available.

## Slide 11
Introduce QCM with more robust coating material (Al2O3):
  Higher melting temperature (340dC higher)
  Higher chemical stability
    no chemical reaction w. contaminants